## Slide 1: Raspberry Pi Sensor and Security More Fun with Pi
By Chuck Duey
Feb 13th 2019
TM Raspberry Pi Foundation www.raspberrypi.org

## Slide 2: This is What We are Doing Today

## Slide 3: Outline:
Tips and Tools for the Raspberry Pi
Somethings the Raspberry Pi can do with USB hardware
  Wireless router/Access point
  Software Defined Radio…Show FM and TCAS
Raspberry Pi Addon Hardware
  Built in interfaces for camera and display
  Hats and bonnets
  Other Addon Boards
Detailed tour of the I/O ports and how to connect.
GPIO Relay and Buttons…Linux, Python.
I2C Devices. Look at display
I2C Devices Look at Pressure sensor 4 ways. Linux, Python, smbus and MRAA.
Look at SPI compare SPI to I2C.
ADC to Display.
Sockets and communications
TM Raspberry Pi Foundation www.raspberrypi.org

## Slide 4: Difference between the Raspberry Pi Versions
Model | Zero/W | B | Pi 3 A+ | B+ | Pi 2 | Pi 3 | Pi 3+
CPU | Arm 6 1000MHz | Arm 6 700MHz | 4xArm 53 1400MHz | Arm 6 700MHz | 4xArm 7 900MHz | 4xArm 8 1200MHz | 4xArm 53 1400MHz
RAM | 512MB | 512MB | 512MB | 512MB | 1GB | 1GB | 1GB
USB | 1 | 2 | 1 | 4 | 4 | 4 | 4
Network | None/WiFi | 10/100 | WiFi | 10/100 | 10/100 | 10/100/WiFi | 10/300/WiFi
Video | HDMI | HDMI/NTSC/PAL | HDMI/NTSC/PAL | HDMI/NTSC/PAL | HDMI/NTSC/PAL | HDMI/NTSC/PAL | HDMI/NTSC/PAL
Hardware IO | 25 | 17 | 25 | 25 | 25 | 25 | 25
+5V Current | 120mA | 350mA | 300mA | 250mA | 350mA | 480mA | 600mA
Bluetooth | Yes/W | No | Yes | No | No | Yes | Yes
SD Card | Micro | Mini | Micro | Micro | Micro | Micro | Micro
Cost | $5/$10* | $30* | $25 | $25 | $35 | $35 | $35

## Slide 5
A+
B
Zero
B+
Pi2
Pi3
Pi3+
Zero W

## Slide 6: Some Raspberry Pi Resources
TM Raspberry Pi Foundation www.raspberrypi.org
Good Links and web sites:
www.raspberrypi.org —The Foundation’s Website
www.raspberrypi.org/downloads — Various Raspberry Pi Operating Systems
www.adafruit.com — Adafruit very good site for parts and tutorials
learn.adafruit.com/category/raspberry-pi —Many projects and how to’s at Adafruit
www.sparkfun.com —Raspberry Pi parts and many other Hobby parts. (Colorado Co.)
www.mcmelectronics.com —Low priced Raspberry Pi Parts
www.microcenter.com —Online and In Store Raspberry Pi
http://www.instructables.com/howto/Raspberry+Pi/ Lots of good Pi Tutorials
https://github.com/Chuckduey/CSU_Pi_Class.git GitHub page with the code from this class.
My email cduey@msn.com

## Slide 7: Important Raspberry Pi Tips
Do Not add or remove hardware while running. Including USB devices. Plugging in a mouse at the last minute can kill the SD card.
Power down the Raspberry Pi using a software command before removing power. SD corruption is very common on uncontrolled power downs.
SD cards are fragile and also wear out. Keep a backup copy of your code. It is best to store it on a network drive.
SD cards come in various speeds and sizes. Class 10 is the fastest. For the Raspberry Pi 32GB is the maximum sized. (SD limitation)
The Raspberry Pi I/O ports are 3.3V. A 5V signal will render the port, and possibly the whole Pi useless.
The Micro SD cards are very easy to pop out accidentally. If it does while it is running, resist the temptation to plug it right back in. Power down first!!!

## Slide 8: Useful Tools
Linux or MAC computer with USB and network.
  With a Linux computer, it makes it easy to copy, change and back up Raspberry Pi SD cards using the “dd” command.
  Also the ssh, and ssh –X makes it easy to remote in to work.
Win32 Disk Imager - A perfect tool copying and backing up Raspberry Pi SD cards. Do not do a direct SD to SD copy.
PuTTY - creates a terminal window that can be used to “ssh” to any Linux computer on you network from a windows machine.
VNC/ RealVNC – VNC can display a desktop to another computer Linux or Windows. Very nice for remote work from different platforms.
USB power 2A or more - While most computers are limited to 500mA of current on the USB port, it is easy to have more that that draw from a Raspberry Pi with accessories.

## Slide 9: WinSCP File browser between Pi an PC

## Slide 10: Open a Pi Terminal
Click Here

## Slide 11: Terminal window commands
ls = list files in directory ls –l = List long ls –a = List all
cd (dir name) = change directory
df –h = Show file systems sizes and usage
nano (file) = Simple intuitive text editor
vi (file) = Simple powerful non-intuitive test editor.
cat (file) = output the contents of a file
less (file) = output a file one page at a time
apt-get install (package) = get an package to install
apt-get update = update packages
apt-cache show (key word) = show available packages
sudo = next command execute as root
ifconfig = show the ip interface connections

## Slide 12: Text Editor with Code Context “Geany”

## Slide 13: Raspberry Pi as Wireless Access Point
https://learn.adafruit.com/setting-up-a-raspberry-pi-as-a-wifi-access-point?view=all

## Slide 14: Raspberry Pi I/O*
GPIO
  Good for Controlling devices like relays, LEDs etc.
  Also can be used as inputs. Can be made to implement bus system.
UART/Serial – 2 Wire interface 3.3V
  Good for GPS, RS-232 Monitor, and many others.
  Baud rates up to 115200 bps
SPI Serial 4 Wire interface. (MOSI, MISO, SCLK, CE) 3.3V
  2 Chip Selects built in. Easy connections to many serial sensors.
  Speeds can be between 8KHz to 125MHz
  This can be used to run an LCD Screen
I2C Serial 2 Wire Interface. (SDA, SDL) 3.3V
  Multiple devices with 7 bit address. Up to 127 - 11
  Much slower 400Kbps For Raspberry Pi.
  Great for touch screen sensors.

## Slide 15: GPIO Pin out*
*From http://pi.gadgetoid.com/pinout
Note: GPIO pins are 3.3V Only
A 5V input will cause damage to the Raspberry Pi!!!
Pi A and B Pin Out
All Others Extra pins

## Slide 16: Now For Fun and Games with the Pi

## Slide 17: Hook up Relay
Connect Relay to Pin 3 of J9
Connect VDD to +5VSYS on J10, and GND on the same J9

## Slide 18: Geany looper.sh and LED_Blink.py
Run “python LED_Blink.py” first then “./looper.sh”

## Slide 19: Web Page LED Control
Click Here
Turn on and off your Relay

## Slide 20: Geany button.py, button_demo.py and button.pwm.py
python button.py - Press buttons….Senses but it is a polling routine
python button_demo.py - Buttons now are set up as events.

## Slide 21: I2C Bus and Tools
The i2c bus is a bidirectional bus with 2 lines SDA and SCL.
This bus can have up to 117 devices.
i2cdetect - Show the devices on an i2c bus
i2cget – read a register value from an i2c device
i2cset – write a value to an i2cdevice.
i2cdump – dump all the values available from an i2cdevice.

## Slide 22: Hook up the I2C Pressure temp sensor
Connect J11 GND to Ground on Pressure sensor
Connect J11 VSENSOR to VDD on Pressure sensor
Connect J11 SCL to SCL and SDA to SDA
I2cdetect –y 1 - You should see if it is correct

## Slide 23: i2cdetect –y 1 – and see if it is hooked up
i2cset –y 1 0x60 0x26 0xb9 :dump again
i2cdump –y 1 0x60 i :look at the values

## Slide 24: Geany pressure.py : See the output of the Pressure sensor

## Slide 25: Look at a whole other i2c bus
i2cdetect –y 0

## Slide 26: Geany LCD_basic.py – Explore i2c LCD

## Slide 27: Geany LCD_call_fun.py – Python Function

## Slide 28: SPI and ADC
The SPI interface is a much higher speed interface than the I2C. This uses 4 lines. MOSI, MISO, CLK, and CS.
Here we will be using the MCP3208 ADC on the SPI Bus.
Hook up the Analog Temperature sensor. Connect TEMP to J10 “A6” Pin for the analog input
Hook up VDD to J12 VSENSOR and GND to the same J12

## Slide 29: Open adc_test.c with Geany, compile, link, and run

## Slide 30: IOT Security
0. Do not use Default Passwords
1. Never store plain text passwords use MD5/SHA hash.
2. Wireless use encryption. (WEP)
3. Use secure sockets when communicating beyond local
network. HTTPS over HTTP. ngrok can be used.
4. Only open required sockets.
5. Make sure your socket can take anything. Buffer over
-runs have been used as successful attacks.
TLS/SSL Transport Layer Security / Secure Socket Layer

## Slide 31: Communicating Via Sockets
In Geany open up socket_server.py, socket_client.py and socket_cl_addr.py
In one terminal start up the Socket Server “python socket_server.py”
In a different terminal run a “ python socket_client.py” and send a message.

## Slide 32: Now for some fun over the LAN
Find your IP address by typing “ifconfig” Trade addresses with neighbors
Then use “python socket_cl_addr.py” to send data to your neighbor.
This is a nmap probe looking at this port.
If there is an open port, be prepared for it to be probed!

## Slide 33: When Ever Opening a Port Make it Resilient

## Slide 34: Different reserved port functions
21 – FTP File Transfer Protocol
22 – SSH/SCP – SSL/TLS Secure Socket Layer
23 – Telnet – Unencrypted communications
80 – HTTP – Primary HTTP port
443 – HTTPS – HTTP over SSL/TLS Encrypted connection
  *Requires third party certificate to authenticate.
We will need stop the existing web services: Type
sudo service apache2 stop

## Slide 35: Looking at basic HTML and Serving via Request Response Cycle
Geany hello.html and hello_web.py
sudo python hello_web.py

## Slide 36: In a Web browser open localhost

## Slide 37: Share ip addresses and open other lab station webpages

## Slide 38: There observer on the network

## Slide 39: Wireshark Data Capture HTTPS via ngrok

## Slide 40: Even running on the Pi, the Data cannot be read

## Slide 41: Explore and Hack with the code and sensors
Make the Pressure Sensor display on the LCD
Make a settable thermostat using the buttons, thermo sensor and relay.
Make a Temp and Barometer display with Rising / Falling pressure.
gcc -shared –I /usr/include/python2.7/ -l python2.7 -l mraa -o adcPythonC.so adcPythonC.c

## Slide 42: Thanks !!! Have Fun With Raspberry Pi