## Slide 1: Basic Raspberry Pi and embedded systems
By Chuck Duey
February 26th 2021
TM Raspberry Pi Foundation www.raspberrypi.org

## Slide 2: Outline:
Your project and programming
Different embedded systems
Raspberry Pi Versions.
Tips and Tools for the Raspberry Pi
How to install and update your own “Distro”
Hook up and tour of the standard Linux desktop
Raspberry Pi Packages
Raspberry Pi and Web and LAMP stack
Somethings the Raspberry Pi can do with USB hardware
Raspberry Pi Addon Hardware
  Built in interfaces for camera and display
  Hats and bonnets
  Other Addon Boards
Hands on exercise running and programming the Raspberry Pi
TM Raspberry Pi Foundation www.raspberrypi.org

## Slide 3: Think About the Scope of Your Project
Many projects try to reach too far. Start simple and improve over the semester.
Think a little ahead on what might be wanted. For example, it is easier to get a board with Wi-Fi than add it later.
Does your project need analog I/O? Some systems have it built in, other need addon boards.
Hardware is only part of the picture; most projects need more time to write and debug the software.
When possible have two of any critical hardware piece. At the last minute, hardware breaks or gets damage.
Do not procrastinate!

## Slide 4: Major Programming Languages

## Slide 5: For More Maker Board Information
https://media.digikey.com/Resources/Maker/the-original-guide-to-boards-2020.pdf

## Slide 6: Standalone Microprocessor
Advantages
Targeted size and function. Right for the job.
Low cost.
Many EVM’s for low cost.
Support from the manufacturer.
Full custom design. Can make very small.
Disadvantages
Need to build circuitry.
Not much Open-source hardware or software
Need to pay for high level language cross compilers.
TI LaunchPad™ Development Kit

## Slide 7: Arduino
Advantages
Many different I/O’s built-in including ADC.
Very nice IDE. (Integrated Development Environment)
Huge opensource community for both hardware and software.
Many premade shields and hardware addons.
Disadvantages
ADC lower resolution and slow. Difficult to do audio speeds.
Need to get a Wi-Fi/BT version in advance, or add on for IOT
Not easy to get a high-resolution dynamic display.

## Slide 8: Teensy and Other Small Variants
Arduino like IDE and programming.
Many with Analog I/O.
Very small and low power.
More difficult to prototype with.
ADC lower resolution and slow. Difficult to do audio speeds.
Need to get a Wi-Fi/BT version in advance, or add on for IOT
SparkFun Artemis
Adafruit
Circuit Playground
Teensy 3.2

## Slide 9: BeagleBone
Advantages
Linux operating system. Can program in many languages and interact with the internet.
Can make Webpages and run full LAMP stack.
Open-source software and hardware support.
Fast ARM core processor.
The Black Version has a micro-HDMI display.
Analog inputs!!!
Disadvantages
Display resolution not that good.
Single Core ARM Processors.
Operating system overhead.
Costs more than Raspberry Pi
Community support is not as wide as Raspberry Pi
Operating system and Overlays not stable.

## Slide 10: Nvidia Jetson Family
Advantages
Ubuntu Linux Operating System
Open-source software and hardware support.
Industrial use and quality
Fast ARM core processors and GPU.
Uses same 40 pin connector as Raspberry Pi.
Disadvantages
Cost for higher end units >$300.00
Need to add on hardware for Analog inputs.
Power hungry when compared to other micro controllers.
Operating system overhead.
40 pin connector rotated 180 degrees from Raspberry Pi.

## Slide 11: Time to talk about Raspberry Pie

## Slide 12: Raspberry Pi
Advantages
Linux operating system. Can program in many languages and interact with the internet.
Can make Webpages and run full LAMP stack.
Massive open-source software and hardware support.
Very fast ARM core processor.
Easy to implement GUI’s for interactive programs.
Disadvantages
Need to add on hardware for Analog inputs.
Power hungry when compared to other micro controllers.
Operating system overhead.
Heat dissipation on newer versions

## Slide 13: Difference between the Raspberry Pi Versions
Model | B | B+ | Pi 2 | Zero/W | Pi 3 A+ | Pi 3+ | Pi 4 | Pi 400
CPU | Arm 6 700MHz | Arm 6 700MHz | 4xArm 7 900MHz | Arm 6 1000MHz | 4xArm 53 1400MHz | 4xArm 53 1400MHz | 4xArm 72 1500MHz | 4xArm 72 1800MHz
RAM | 512MB | 512MB | 1GB | 512MB | 512MB | 1GB | 1GB/2GB/4GB/8GB | 4GB
USB | 2 | 4 | 4 | 1 | 1 | 4 | 2-2.0 2-3.0 | 1-2.0 2-3.0
Network | 10/100 | 10/100 | 10/100 | None/Wi-Fi | Wi-Fi | 10/300 Wi-Fi abg | 10/100/1G Wi-Fi abg | 10/100/1G Wi-Fi abg
Video | HDMI/NTSC/PAL | HDMI/NTSC/PAL | HDMI/NTSC/PAL | HDMI | HDMI/NTSC/PAL | HDMI/NTSC/PAL | 2xHDMI NTSC/PAL | 2xHDMI
Hardware IO | 17 | 25 | 25 | 25 | 25 | 25 | 25 | 25
+5V Supply | 1A | 1A | 1.5A | 500mA | 1A | 2.5A | 3.0A | 3.0A
Bluetooth | No | No | No | Yes/W | Yes | Yes | Yes | Yes
SD Card | Mini | Micro | Micro | Micro | Micro | Micro | Micro | Micro
Cost | $30 | $25 | $35 | $5/$10 | $25 | $35 | $35/$45/$55 | $70

## Slide 14: CPU Speed Benchmarks

## Slide 15
A+
B
Zero
B+
Pi2
Pi3
Pi3+
Zero W
Pi4
Pi 400
Which Pi Do you have?

## Slide 16: Some Raspberry Pi Resources
TM Raspberry Pi Foundation www.raspberrypi.org
Good Links and web sites:
www.raspberrypi.org —The Foundation’s Website
www.raspberrypi.org/downloads — Various Raspberry Pi Operating Systems
www.tomshardware.com – Good Linux and Pi tutorials and reviews.
www.adafruit.com — Adafruit very good site for parts and tutorials
learn.adafruit.com/category/raspberry-pi —Many projects and how to’s at Adafruit
www.sparkfun.com —Raspberry Pi parts and many other Hobby parts. (Colorado Co.)
www.newark.com —Low priced Raspberry Pi Parts
www.microcenter.com —Online and In Store Raspberry Pi
www.instructables.com/howto/Raspberry+Pi/ Lots of good Pi Tutorials
https://github.com/Chuckduey/CSU_Pi_Class.git GitHub page with the code from this class.
My email cduey@msn.com

## Slide 17: Important Raspberry Pi Tips
Do Not add or remove hardware while running. Including USB devices. Plugging in a mouse at the last minute can kill the SD card.
Power down the Raspberry Pi using a software command before removing power. SD corruption is very common on uncontrolled power downs.
SD cards are fragile and also wear out. Keep a backup copy of your code. It is best to store it on a network drive.
SD cards come in various speeds and sizes. Class 10 is the fastest. For the Raspberry Pi 32GB is the maximum sized. (SD limitation)
The Raspberry Pi I/O ports are 3.3V. A 5V signal will render the port, and possibly the whole Pi useless.
The Micro SD cards are very easy to pop out accidentally. If it does while it is running, resist the temptation to plug it right back in. Power down first!!!

## Slide 18: Raspberry Pi Raspbian Versions
Initial Release Date | Current Release Name | Debian Version | Linux Kernel | GCC | apt | X Server | Raspberry Pi 1/1+ | Raspberry Pi 2 | Raspberry Pi 3 | Raspberry Pi 3+ | Raspberry Pi 4 | Raspberry Pi 400
2013-09-27 | 2015-05-05 | 7 (Wheezy) | 3.18 | 4.7.2 | 0.9.7 | 7.7 |  |  |  |  |  | 
2015-09-28 | 2017-07-05 | 8 (Jessie) | 4.9 | 4.9 | 1.0.9.8.1 | 7.7 |  |  |  |  |  | 
2017-09-08 | 2019-04-08 | 9 (Stretch) | 4.14 | 6.3 | 1.4.9 | 7.7 |  |  |  |  |  | 
2019-06-24 | 2021-01-11 | 10 (Buster) | 5.4.83 | 8.3 | 1.8.2.2 | 7.7 |  |  |  |  |  | 
Buster
©
Bullseye

## Slide 19: How do you create SD Card Images
www.raspberrypi.org/software/

## Slide 20: Install Raspian
!
Set US Keyboard!

## Slide 21: More installation

## Slide 22: After Reboot

## Slide 23: More Configuration
Camera if you have one
SSH for PuTTY and to transfer files
VNC for remote desktop
SPI for Fast Serial HW
I2C For slower serial HW
Serial Port for HW serial
Serial Console
1-Wire Single wire HW
Remote GPIO
If the keyboard or Time Zone is not set correctly
For systems with more the 2GB RAM – Increase GPU Memory

## Slide 24: Useful Tools
Linux or MAC computer with USB and network.
  With a Linux computer, it makes it easy to copy, change and back up Raspberry Pi SD cards using the “dd” command.
  Also the ssh, and ssh –X makes it easy to remote in to work.
Win32 Disk Imager - A perfect tool copying and backing up Raspberry Pi SD cards. Do not do a direct SD to SD copy.
PuTTY - creates a terminal window that can be used to “ssh” to any Linux computer on you network from a windows machine.
VNC/ RealVNC – VNC can display a desktop to another computer Linux or Windows. Very nice for remote work from different platforms.
USB power 3.0A or more - While most computers are limited to 500mA of current on the USB port, it is easy to have more that that draw from a Raspberry Pi with accessories.

## Slide 25: VNC – Remote access desktop
https://www.realvnc.com/en/connect/download/viewer/ - Download a viewer
Hover over network symbol in upper right to find address

## Slide 26: VNC to Your Pi from Anywhere
For Remote access set up an account. https://www.realvnc.com/en/raspberrypi/
Sign in once an account is created

## Slide 27: WinSCP
https://winscp.net/eng/download.php

## Slide 28: Using WinSCP
IP Address of Pi
Set to SCP

## Slide 29: Useful Windows Tools

## Slide 30: Quick Word on SD Cards They are not all the same.
Backup your files!!!! SD Cards will get corrupted.
When you copy an image, actual SD card size can vary by more than a GB. To burn to a new card the image size or bigger is needed! Both Windows and Linux copies will have this problem
If Linux dd is used, make sure to copy the root image. /dev/sdX not /dev/sdX0,1..

## Slide 31: New Backup Tool SD Card Copier
Make a backup of your system. Copy From /dev/mmcblk0 never to!

## Slide 32: Hooks ups for your Raspberry Pi
1. HDMI
2. USB
3. Power
10/100/1000 Network
Audio/Analog Video

## Slide 33: Hook up your Raspberry Pi
Round up the components. Pi, HDMI cable and display, power supply, power cable, USB mouse and USB keyboard.
Plug in the HDMI to the display and Raspberry Pi.
Plug in USB mouse and keyboard.
Plug in power cable on Raspberry Pi end, and then plug in power.
Watch HDMI display and make sure it is booting.
If it is not booting unplug power and check the SD card.
Do not Plug in or remove hardware components while the Pi is powered! It can cause flash corruption.

## Slide 34: Raspberry Pi Raspian Buster

## Slide 35: Terminal Window
Click here once

## Slide 36: Terminal window commands
ls = list files in directory ls –l = List long ls –a = List all
cd (dir name) = change directory
df –h = Show file systems sizes and usage
nano (file) = Simple intuitive text editor
vi (file) = Simple powerful non-intuitive text editor.
cat (file) = output the contents of a file
less (file) = output a file one page at a time
apt install (package) = get a package to install
apt update = update packages
apt-cache show (key word) = show available packages
sudo = next command execute as root
ifconfig = show the ip interface connections
https://www.tomshardware.com/reviews/raspberry-pi-command-line-commands,6159.html

## Slide 37: Ways to get applications and software packages
apt-cache search [package]
sudo apt install [package] octave, mysql, git, python-pip…
pip install ‘Some Application’
sudo easy_install –U [Python Package] spidev, Rpi.GPIO
git clone git://[package site] git.osmocom.org/rtl-sdr-git
Download “tgz” file. tar –xzf package.tgz

## Slide 38: GitHub Collaboration Tools

## Slide 39: Hello World! Geany
Change the code, save and run it.

## Slide 40: Hello World! Geany
Then Run it
Compile the code

## Slide 41: Connect to internet and download package
Open a web page to www.google.com
Open a terminal and “apt-cache search spice”
sudo apt install oregano
<- install oregano spice simulation program ->
Verify Connection to Wireless

## Slide 42: Matlab® and Raspberry Pi
Matlab only runs on PC, or other Intel/AMD computers.
Matlab can connect and run commands that controls hardware.
The Student version of Matlab comes with all the controls, many tool boxes and Simulink.
The Student version can ONLY be used by students to meet course requirements and perform research at degree granting institutions.
>> rpi = raspi(‘Address',‘User',‘Password');
>> mcp3208 = spidev(rpi, 'CE0');
>> for i=1:8
[v(i),t(i)] = DAC_Read(mcp3208,i);
end
>> t
t = 66.4532 65.7501 67.1563 66.5411 67.0684 67.1563 67.5958 67.7716
>> scanI2CBus(rpi,'i2c-1')
ans = 1×4 cell array
'0x20' '0x39' '0x3E' '0x68'

## Slide 43: Web Pages
It is very easy to set up a Raspberry Pi to serve Web Pages
Open a web browser and go to “localhost” click on the “Pi_User_Test_Page” link
Now in a terminal window
cd CSU_Pi_Class/html
edit the test.html file in your home directory using nano.
nano test.html
<ctl-o><ctl-x> to save
Refresh the webpage to
See your edits.

## Slide 44: Full LAMP Stack (Linux Apache MySQL PHP)

## Slide 45: GUI’s via Python Tkinter, Pygame, Qt, GTK+ and Wx Widgets

## Slide 46: Add on Hardware
USB:
  SDR Radios – Can receive AM, FM, SSB, Aircraft and Satellites
  GPS – add precise time and location.
  Instrument control. – Control Lab meters, oscilloscope and more.
  Connect to Arduinos or other embedded devices.
DSI Interface – Raspberry Pi unique interface.
  Camera – right now up to an 8M pixel camera. Full color or No IR.
  Display – Very nice 7” touch screen is all that is supported now.
Hats – 40 pin interface to hardware.
  Best way to get ADCs and DACs.
  Many control boards for relays and LED signs
  With ADC’s, DAC’s and GPIO expanders a brewery controller.

## Slide 47: Raspberry Pi as Wireless Access Point
https://learn.adafruit.com/setting-up-a-raspberry-pi-as-a-wifi-access-point?view=all
Addon Hardware

## Slide 48: SDR and GNURadio Example
Addon Hardware

## Slide 49: GNURadio and Raspberry Pi 10.5 GHz Radar Test Range
Addon Hardware

## Slide 50: One more SDR Example Receiving NOAA Satellite Data
http://www.instructables.com/id/Raspberry-Pi-NOAA-Weather-Satellite-Receiver/
Addon Hardware

## Slide 51: Touch Screen from RPi Foundation
Addon Hardware

## Slide 52: Addon Hardware Pi Camera – uses built in port.
Addon Hardware

## Slide 53: Raspberry Pi I/O*
UART/Serial – 2 Wire interface 3.3V
  Good for GPS, RS-232 Monitor, and many others.
  Baud rates up to 115200 bps
SPI Serial 4 Wire interface. (MOSI, MISO, SCLK, CE) 3.3V
  2 Chip Selects built in. Easy connections to many serial sensors.
  Speeds can be between 8KHz to 125MHz
  This can be used to run an LCD Screen
I2C Serial 2 Wire Interface. (SDA, SDL) 3.3V
  Multiple devices with 7 bit address. Up to 127 - 11
  Much slower 400Kbps For Raspberry Pi.
  Great for touch screen sensors.
* From www.raspberrypi.org/forums

## Slide 54: GPIO Pin out*
*From http://pi.gadgetoid.com/pinout
Note: GPIO pins are 3.3V Only
A 5V input will cause damage to the Raspberry Pi!!!

## Slide 55: Pi Hats – Hardware for the Raspberry Pi

## Slide 56: Other Addon Boards
Cirrus Logic Audio Card
Gertboard
Pimoroni DAC Bonnet
Adafruit OLED Bonnet
Adafruit Proto Bonnet

## Slide 57: Franken Chiller Brewery Control

## Slide 58: Now For Fun and Games with the Pi

## Slide 59: Looking at the I2C bus HTS221
i2cdetect –y 1
i2cdump –y 1 0x5f
Humidity registers = 0x29 0x28
Temperature registers = 0x2b 0x2a

## Slide 60: More I2C Fun
i2cget –y 1 0x5f 0x20
i2cset –y 1 0x5f 0x20 0x81
i2cget –y 1 0x5f 0x20
i2cdump –y 1 0x5f
Humidity registers = 0x29 0x28
Temperature registers = 0x2b 0x2a

## Slide 61: Geany – A Good Generic Programming IDE

## Slide 62: Accelerometer.
Type: Open accel.py in Geany
Hit Run and tilt the Pi

## Slide 63: Weather station
Inside Geany open the MiniWeatherStation.py

## Slide 64: Copy and pasting between windows.
In a terminal window type: python
Select from Geany, go to Python window and center click:
>>> from sense_hat import SenseHat
>>> sense = SenseHat()
>>> sense.clear()
>>> sense.show_message(“Your Message”, text_colour=[255, 0, 0])
When done.
>>> exit()

## Slide 65: Sense Hat – Chuck Maze
Use Default Maze

## Slide 66: Pi Sense Hat – Chuck Paint

## Slide 67: Arduino and Raspberry Pi
One interesting addition that can be made is to use an Arduino platform for low level hardware control. The Raspberry Pi has the fast graphical display.
Connect the Circuit Playground to one of the USB ports of the Raspberry Pi.

## Slide 68: Open Arduino IDE
Double click and Execute
Open Serial Monitor

## Slide 69: Arduino to Pi Communication
Open monitor
Enter LED# + RGB code
Serial data coming to the Pi

## Slide 70: Run the game_circle.py app.
What happens when it is leveled

## Slide 71: GitHub – Great Collaboration Tool
For opensource projects it is Free.
Size limit is 1GB, and no file bigger than 100MB.
You can start a Repository and control who can change it.
Changes can be made and tracked.
Branches of code and Tags can be generated.
Private Repos and Closed Repos can be made, but require a monthly fee.
It is a great way to have an opensource project with collaboration.

## Slide 72: Fun with Octave
Exit When done.
>> sin_plot

## Slide 73: Thanks !!! Have Fun With Raspberry Pi
Code is available at https://github.com/Chuckduey/CSU_Pi_Class.git