## Slide 1: Basic Raspberry Pi and embedded systems
By Chuck Duey
February 26th, 2021
TM Raspberry Pi Foundation www.raspberrypi.org

## Slide 2: Outline:
Your project and programming
Different embedded systems
Raspberry Pi Versions.
Tips and Tools for the Raspberry Pi
How to install and update your own “Distro”
Hook up and tour of the standard Linux desktop
Raspberry Pi Packages
Raspberry Pi and Web and LAMP stack
Somethings the Raspberry Pi can do with USB hardware
Raspberry Pi Addon Hardware
  Built in interfaces for camera and display
  Hats and bonnets
  Other Addon Boards
Hands on exercise running and programming the Raspberry Pi
TM Raspberry Pi Foundation www.raspberrypi.org

## Slide 3: Think About the Scope of Your Project
Many projects try to reach too far. Start simple and improve over the semester.
Think a little ahead on what might be wanted. For example, it is easier to get a board with Wi-Fi than add it later.
Does your project need analog I/O? Some systems have it built in, other need addon boards.
Hardware is only part of the picture; most projects need more time to write and debug the software.
When possible have two of any critical hardware piece. At the last minute, hardware breaks or gets damage.
Do not procrastinate!

## Slide 4: Major Programming Languages

## Slide 5: For More Maker Board Information
https://media.digikey.com/Resources/Maker/the-original-guide-to-boards-2020.pdf

## Slide 6: Standalone Microprocessor
Advantages
Targeted size and function. Right for the job.
Low cost.
Many EVM’s for low cost.
Support from the manufacturer.
Full custom design. Can make very small.
Disadvantages
Need to build circuitry.
Not much Open-source hardware or software
Need to pay for high level language cross compilers.
TI LaunchPad™ Development Kit

## Slide 7: Arduino
Advantages
Many different I/O’s built-in including ADC.
Very nice IDE. (Integrated Development Environment)
Huge opensource community for both hardware and software.
Many premade shields and hardware addons.
Disadvantages
ADC lower resolution and slow. Difficult to do audio speeds.
Need to get a Wi-Fi/BT version in advance, or add on for IOT
Not easy to get a high-resolution dynamic display.

## Slide 8: Teensy and Other Small Variants
Arduino like IDE and programming.
Many with Analog I/O.
Very small and low power.
More difficult to prototype with.
ADC lower resolution and slow. Difficult to do audio speeds.
Need to get a Wi-Fi/BT version in advance, or add on for IOT
SparkFun Artemis
Adafruit
Circuit Playground
Teensy 3.2

## Slide 9: BeagleBone
Advantages
Linux operating system. Can program in many languages and interact with the internet.
Can make Webpages and run full LAMP stack.
Open-source software and hardware support.
Fast ARM core processor.
The Black Version has a micro-HDMI display.
Analog inputs!!!
Disadvantages
Display resolution not that good.
Single Core ARM Processors.
Operating system overhead.
Costs more than Raspberry Pi
Community support is not as wide as Raspberry Pi
Operating system and Overlays not stable.

## Slide 10: Nvidia Jetson Family
Advantages
Ubuntu Linux Operating System
Open-source software and hardware support.
Industrial use and quality
Fast ARM core processors and GPU.
Uses same 40 pin connector as Raspberry Pi.
Disadvantages
Cost for higher end units >$300.00
Need to add on hardware for Analog inputs.
Power hungry when compared to other micro controllers.
Operating system overhead.
40 pin connector rotated 180 degrees from Raspberry Pi.
AGX $599
Nano $59
NX $399

## Slide 11: Time to talk about Raspberry Pie

## Slide 12: Raspberry Pi
Advantages
Linux operating system. Can program in many languages and interact with the internet.
Can make Webpages and run full LAMP stack.
Massive open-source software and hardware support.
Very fast ARM core processor.
Easy to implement GUI’s for interactive programs.
Disadvantages
Need to add on hardware for Analog inputs.
Power hungry when compared to other micro controllers.
Operating system overhead.
Heat dissipation on newer versions

## Slide 13: Difference between the Raspberry Pi Versions
Model | B | B+ | Pi 2 | Zero/W | Pi 3 A+ | Pi 3+ | Pi 4 | Pi 400
CPU | Arm 6 700MHz | Arm 6 700MHz | 4xArm 7 900MHz | Arm 6 1000MHz | 4xArm 53 1400MHz | 4xArm 53 1400MHz | 4xArm 72 1500MHz | 4xArm 72 1800MHz
RAM | 512MB | 512MB | 1GB | 512MB | 512MB | 1GB | 1GB/2GB/4GB/8GB | 4GB
USB | 2 | 4 | 4 | 1 | 1 | 4 | 2-2.0 2-3.0 | 1-2.0 2-3.0
Network | 10/100 | 10/100 | 10/100 | None/Wi-Fi | Wi-Fi | 10/300 Wi-Fi abg | 10/100/1G Wi-Fi abg | 10/100/1G Wi-Fi abg
Video | HDMI/NTSC/PAL | HDMI/NTSC/PAL | HDMI/NTSC/PAL | HDMI | HDMI/NTSC/PAL | HDMI/NTSC/PAL | 2xHDMI NTSC/PAL | 2xHDMI
Hardware IO | 17 | 25 | 25 | 25 | 25 | 25 | 25 | 25
+5V Supply | 1A | 1A | 1.5A | 500mA | 1A | 2.5A | 3.0A | 3.0A
Bluetooth | No | No | No | Yes/W | Yes | Yes | Yes | Yes
SD Card | Mini | Micro | Micro | Micro | Micro | Micro | Micro | Micro
Cost | $30 | $25 | $35 | $5/$10 | $25 | $35 | $35/$45/$55 | $70

## Slide 14: CPU Speed Benchmarks

## Slide 15
A+
B
Zero
B+
Pi2
Pi3
Pi3+
Zero W
Pi4
Pi 400
Which Pi Do you have?

## Slide 16: Some Raspberry Pi Resources
TM Raspberry Pi Foundation www.raspberrypi.org
Good Links and web sites:
www.raspberrypi.org —The Foundation’s Website
www.raspberrypi.org/downloads — Various Raspberry Pi Operating Systems
www.tomshardware.com – Good Linux and Pi tutorials and reviews.
www.adafruit.com — Adafruit very good site for parts and tutorials
learn.adafruit.com/category/raspberry-pi —Many projects and how to’s at Adafruit
www.sparkfun.com —Raspberry Pi parts and many other Hobby parts. (Colorado Co.)
www.newark.com —Low priced Raspberry Pi Parts
www.microcenter.com —Online and In Store Raspberry Pi
www.instructables.com/howto/Raspberry+Pi/ Lots of good Pi Tutorials
https://github.com/Chuckduey/CSU_Pi_Class.git GitHub page with the code from this class.
My email cduey@msn.com

## Slide 17: Important Raspberry Pi Tips
Do Not add or remove hardware while running. Including USB devices. Plugging in heavy load on the USB at the last minute can kill the SD card.
Power down the Raspberry Pi using a software command before removing power. SD corruption is very common on uncontrolled power downs.
SD cards are fragile and wear out. Keep a backup copy of your code. It is best to store it on a network drive.
SD cards come in various speeds and sizes. Class 10 is the fastest. For the Raspberry Pi 32GB is the maximum sized. (SD limitation)
The Raspberry Pi I/O ports are 3.3V. A 5V signal will render the port, and possibly the whole Pi useless.
The Micro SD cards are very easy to pop out accidentally. If it does while it is running, resist the temptation to plug it right back in. Power down first!!!

## Slide 18: Raspberry Pi Raspbian Versions
Initial Release Date | Current Release Name | Debian Version | Linux Kernel | GCC | apt | X Server | Raspberry Pi 1/1+ | Raspberry Pi 2 | Raspberry Pi 3 | Raspberry Pi 3+ | Raspberry Pi 4 | Raspberry Pi 400
2013-09-27 | 2015-05-05 | 7 (Wheezy) | 3.18 | 4.7.2 | 0.9.7 | 7.7 |  |  |  |  |  | 
2015-09-28 | 2017-07-05 | 8 (Jessie) | 4.9 | 4.9 | 1.0.9.8.1 | 7.7 |  |  |  |  |  | 
2017-09-08 | 2019-04-08 | 9 (Stretch) | 4.14 | 6.3 | 1.4.9 | 7.7 |  |  |  |  |  | 
2019-06-24 | 2021-01-11 | 10 (Buster) | 5.4.83 | 8.3 | 1.8.2.2 | 7.7 |  |  |  |  |  | 
Buster
©
Bullseye

## Slide 19: How do you create SD Card Images
www.raspberrypi.org/software/

## Slide 20: Hooks ups for your Raspberry Pi
1. HDMI
2. USB
3. Power
10/100/1000 Network
Audio/Analog Video

## Slide 21: Hook up your Raspberry Pi
Round up the components. Pi, HDMI cable and display, power supply, power cable, USB mouse and USB keyboard.
Plug in the HDMI to the display and Raspberry Pi.
Plug in USB mouse and keyboard.
Plug in power cable on Raspberry Pi end, and then plug in power.
Watch HDMI display and make sure it is booting.
If it is not booting unplug power and check the SD card.
Do not Plug in or remove hardware components while the Pi is powered! It can cause flash corruption.

## Slide 22: Install Raspian
!
Set US Keyboard!

## Slide 23: More installation

## Slide 24: After Reboot

## Slide 25: More Configuration
Camera if you have one
SSH for PuTTY and to transfer files
VNC for remote desktop
SPI for Fast Serial HW
I2C For slower serial HW
Serial Port for HW serial
Serial Console
1-Wire Single wire HW
Remote GPIO
If the keyboard or Time Zone is not set correctly
For systems with more the 2GB RAM – Increase GPU Memory

## Slide 26: Useful Tools
Linux or MAC computer with USB and network.
  With a Linux computer, it makes it easy to copy, change and back up Raspberry Pi SD cards using the “dd” command.
  Also, the ssh, and ssh –X makes it easy to remote in to work.
Win32 Disk Imager - A perfect tool copying and backing up Raspberry Pi SD cards. Do not do a direct SD to SD copy.
PuTTY - creates a terminal window that can be used to “ssh” to any Linux computer on you network from a windows machine.
VNC/ RealVNC – VNC can display a desktop to another computer Linux or Windows. Very nice for remote work from different platforms.
USB power 3.0A or more - While most computers are limited to 500mA of current on the USB port, it is easy to have more that that draw from a Raspberry Pi with accessories.

## Slide 27: VNC – Remote access desktop
https://www.realvnc.com/en/connect/download/viewer/ - Download a viewer
Hover over network symbol in upper right to find address

## Slide 28: VNC to Your Pi from Anywhere
For Remote access set up an account. https://www.realvnc.com/en/raspberrypi/
Sign in once an account is created

## Slide 29: WinSCP
https://winscp.net/eng/download.php

## Slide 30: Using WinSCP
IP Address of Pi
Set to SCP

## Slide 31: Useful Windows Tools

## Slide 32: Quick Word on SD Cards They are not all the same.
Backup your files!!!! SD Cards will get corrupted.
When you copy an image, actual SD card size can vary by more than a GB. To burn to a new card the image size or bigger is needed! Both Windows and Linux copies will have this problem
If Linux dd is used, make sure to copy the root image. /dev/sdX not /dev/sdX0,1..

## Slide 33: New Backup Tool SD Card Copier
Make a backup of your system. Copy From /dev/mmcblk0 never to!
While the copy is running close all other applications and do not make any changes to the file system.

## Slide 34: Raspberry Pi Raspian Buster

## Slide 35: Terminal Window
Click here once

## Slide 36: Terminal window commands
ls = list files in directory ls –l = List long ls –a = List all
cd (dir name) = change directory
df –h = Show file systems sizes and usage
nano (file) = Simple intuitive text editor
vi (file) = Simple powerful non-intuitive text editor.
cat (file) = output the contents of a file
less (file) = output a file one page at a time
apt install (package) = get a package to install
apt update = update packages
apt-cache show (key word) = show available packages
sudo = next command execute as root
ifconfig = show the ip interface connections
https://www.tomshardware.com/reviews/raspberry-pi-command-line-commands,6159.html

## Slide 37: Ways to get applications and software packages
apt-cache search [package]
sudo apt install [package] octave, mysql, git, python-pip…
pip install ‘Some Application’
sudo easy_install –U [Python Package] spidev
git clone git://[package site] git.osmocom.org/rtl-sdr-git
Download “tgz” file. tar –xzf package.tgz

## Slide 38: *Connect to internet and download package
Open a web page to www.google.com
Open a terminal and “apt-cache search spice”
sudo apt install oregano
<- install oregano spice simulation program ->
Verify Connection to Wireless

## Slide 39: Alterative GUI method Preferences -> Add/Remove Software

## Slide 40: *GitHub Collaboration Tools
https://github.com/Chuckduey/CSU_Pi_Class
git clone <Center Click>
Left Mouse Click
git pull
This will get the latest release of the files.

## Slide 41: GitHub – Great Collaboration Tool
For opensource projects it is Free.
Size limit is 500MB, and no file bigger than 100MB.
You can start a repository and control who can change it.
Changes can be made and tracked.
Branches of code and Tags can be generated.
Private Repos and Closed Repos can be made but require a monthly fee.
It is a great way to have an opensource project with collaboration.
A good basic class:

## Slide 42: GitHub – Great Collaboration Tool
For opensource projects it is Free.
Size limit is 1GB, and no file bigger than 100MB.
You can start a repository and control who can change it.
Changes can be made and tracked.
Branches of code and Tags can be generated.
Private Repos and Closed Repos can be made, but require a monthly fee.
It is a great way to have an opensource project with collaboration.
A good basic class: https://www.coursera.org/learn/introduction-git-github

## Slide 43: Example of GitHub Desktop

## Slide 44: *Geany – A Good Generic Programming IDE

## Slide 45: *Hello World! Geany
Change the code, save and run it.

## Slide 46: *Hello World! Geany
Then Run it
Compile the code

## Slide 47: Raspberry Pi I/O*
GPIO – General Purpose I/O
  Good for LED and Relay Control
  Input good to sense buttons and switches
UART/Serial – 2 Wire interface 3.3V
  Good for GPS, RS-232 Monitor, and many others.
  Baud rates up to 115200 bps
SPI Serial 4 Wire interface. (MOSI, MISO, SCLK, CE) 3.3V
  2 Chip Selects built in. Easy connections to many serial sensors.
  Speeds can be between 8KHz to 125MHz (1MHz default)
  This can be used to run an LCD Screen
I2C Serial 2 Wire Interface. (SDA, SDL) 3.3V
  Multiple devices with 7-bit address. Up to 127 - 11
  Much slower 400Kbps For Raspberry Pi.
  Great for touch screen sensors.

## Slide 48: *GPIO Pin out
Note: GPIO pins are 3.3V Only
A 5V input will cause damage to the Raspberry Pi!!!
Note: for Raspberry 4B version 2.52 GPIO is needed
wget https://project-downloads.drogon.net/wiringpi-latest.deb
sudo dpkg -i wiringpi-latest.deb

## Slide 49: *Standard Raspberry PI GPIO functions
-g
-g
looper.sh >>>
#!/bin/bash
gpio mode 7 out
while true; do
gpio write 7 1
sleep 0.5
gpio write 7 0
sleep 0.5
done

## Slide 50: Add on Hardware
USB:
  SDR Radios – Can receive AM, FM, SSB, Aircraft and Satellites
  GPS – add precise time and location.
  Instrument control. – Control Lab meters, oscilloscope and more.
  Connect to Arduinos or other embedded devices.
DSI Interface – Raspberry Pi unique interface.
  Camera – right now up to an 8M pixel camera. Full color or No IR.
  Display – Very nice 7” touch screen is all that is supported now.
Hats – 40 pin interface to hardware.
  Best way to get ADCs and DACs.
  Many control boards for relays and LED signs
  With ADC’s, DAC’s and GPIO expanders a brewery controller.

## Slide 51: Touch Screen with Camera and Case
Addon Hardware
https://www.adafruit.com/product/4377

## Slide 52: Addon Hardware Pi Camera – uses built in port.
Addon Hardware

## Slide 53: SDR and GNURadio Example
Addon Hardware

## Slide 54: GNURadio and Raspberry Pi 10.5 GHz Radar Test Range
Addon Hardware

## Slide 55: Pi Hats – Hardware for the Raspberry Pi
Pimoroni DAC Bonnet
Adafruit OLED Bonnet
Adafruit Proto Bonnet

## Slide 56: Franken Chiller Brewery Control

## Slide 57: Raspberry Pi as Wireless Access Point
https://learn.sparkfun.com/tutorials/setting-up-a-raspberry-pi-3-as-an-access-point
Addon Hardware

## Slide 58: Raspberry Pi Sense Hat

## Slide 59: Accelerometer.
Type: Open accel.py in Geany
Hit Run and tilt the Pi

## Slide 60: Sense Hat – Chuck Maze
Use Default Maze

## Slide 61: Weather station
Inside Geany open the MiniWeatherStation.py

## Slide 62: GUIs via Python Tkinter, Pygame, Qt, GTK+ and Wx Widgets

## Slide 63: Pi Sense Hat – Chuck Paint

## Slide 64: Looking at the I2C bus HTS221
i2cdetect –y 1
i2cdump –y 1 0x5f
Humidity registers = 0x29 0x28
Temperature registers = 0x2b 0x2a

## Slide 65: More I2C Fun
i2cget –y 1 0x5f 0x20
i2cset –y 1 0x5f 0x20 0x81
i2cget –y 1 0x5f 0x20
i2cdump –y 1 0x5f
Humidity registers = 0x29 0x28
Temperature registers = 0x2b 0x2a

## Slide 66: Matlab® and Raspberry Pi
MATLAB only runs on PC, or other Intel/AMD computers.
MATLAB can connect and run commands that controls hardware.
The Student version of MATLAB comes with all the controls, many toolboxes and Simulink.
The Student version can ONLY be used by students to meet course requirements and perform research at degree granting institutions. Also, you will need to link to the university license server.
>> rpi = raspi(‘Address',‘User',‘Password');
>> mcp3208 = spidev(rpi, 'CE0');
>> for i=1:8
[v(i),t(i)] = DAC_Read(mcp3208,i);
end
>> t
t = 66.4532 65.7501 67.1563 66.5411 67.0684 67.1563 67.5958 67.7716
>> scanI2CBus(rpi,'i2c-1')
ans = 1×4 cell array
'0x20' '0x39' '0x3E' '0x68'

## Slide 67: Thanks !!! Have Fun With Raspberry Pi
Code is available at https://github.com/Chuckduey/CSU_Pi_Class.git